## Slide 1: Up, Down and Around the Stack: ISP Characterization from Network Intensive Applications
Zachary Bischof, John Otto, Fabián Bustamante
Northwestern University
Notes: Good afternoon, my name is Zachary Bischof. I’m a PhD student at Northwestern University working with Professor Bustamante. Today I’ll be presenting our work, Up, Down, and Around the Stack: ISP Characterization from Network Intensive Applications.

## Slide 2: Broadband characterization
Rapid growth in number of residential broadband subscribers
Characterizing broadband services
  Measurement boxes such as BISmark and SamKnows (UK, US, and now EU)
  Web tests such as Speedtest, Netalyzer
  Measurements from the core Dischinger et al. (IMC07) , Croce et al. (PAM09)
  Measurements from systems at the edge
Notes: Over the past decade, we have seen an unprecedented growth in the adoption of broadband services; today broadband users make up one quarter of the Internet population. However, our ability to measure these networks has not kept pace with their growth.
To address this, several efforts adopting a variety of methods have appeared aiming to shed some much needed light on this problem. Methods range from distributing measurement boxes to end users, such as BISmark and SamKnows, having users run tests in their web browser, such as speedtest and netalyzer, performing measurements from the core of the network, or as we’ve proposed in previous work, performing measurements at systems located on the edge of the network.

## Slide 3: Our approach
Crowdsourcing broadband Characterization to the network Edge (C2E)
  Leverage the views of popular, network-intensive applications running on end systems (e.g. P2P, VoD)
Key advantages
  Capture end users’ experience
  Continuous monitoring combining views of multiple subscribers
  Minimize active measurements
  Application usage can grow with the network edge
Notes:   With our approach, which we refer to as Crowdsourcing broadband characterization to the network Edge, or (C2E), we leverage popular network-intensive applications running on end systems, such as P2P file sharing or video streaming, for the purpose of broadband characterization.
  Some of the benefits of C2E are that it allows us to capture the end users’ actual experience within their application providing an objective point of view. Although each individual user is not continuously running the application, their frequent, repeated use by many, gives us a nearly continuous view for network monitoring. Additionally, by passively monitoring performance within the application, we can avoid the more bandwidth-intensive active measurements, allowing us to reduce the impact of measurements on the user’s network connection and quality of experience. Lastly, C2E’s scalability allows its usage to grow with the network edge. We are able to avoid the high costs involved in the deployment and management of hardware distribution.
  ??? For example, we are able to avoid users who misuse the hardware by flashing a custom firmware for private use.
  http://www.exploitn.com/new-discoveries/13546.htm (one user considers selling their additional free routers)
  https://samknowswrt160nl.wordpress.com/2011/06/24/convert-sam-knows-wrt160nl-to-a-normal-router/ (guide to convert router)

## Slide 4: Studying broadband performance
Previously shown the effectiveness of using network intensive applications for crowdsourcing broadband characterization, but
How well does the performance of network intensive applications relate to other apps?
  And how do they relate to the user?
Notes: We’ve previously shown that C2E is effective at comparing broadband services directly in terms of a particular application, but a key unanswered question is how well the performance characteristics captured by these network-intensive applications can predict the overall user experience with another application. Furthermore, how does it relate to the user experience? In this work, we begin looking at what metrics we can gather from one application and how they relate to the user experience in another. In particular, we’ll be looking at BitTorrent, going to web browsing performance.

## Slide 5: Low level metrics for characterization
Commonly used metrics for last-mile connection
  Bandwidth capacity (download/upload)
  Packet loss
  Latency
  Jitter
We focus on latency and download throughput
  Look at their impact on web browsing performance
Notes: First we need to identify a set of metrics that we can measure from C2E that would be useful for the target application. The most common, well understood metrics for broadband characterization includes download and upload bandwidth, packet loss, latency, and jitter. In this work, we focus on latency and download throughput, looking at their impact on web browsing performance.

## Slide 6: Measuring last-mile latency
Approach
  Capture last mile latency by using traceroute
  Measure latency to the first public IP (that doesn’t belong to the user)
    Will measure further into the network for ISPs that provide a NAT’d IP address
Dataset
  Latency measurements from users in AT&T’s network
  Drop users with a wireless last-meter connection
Notes: First I’ll discuss our latency measurements. We focus on measuring the last-mile latency since we are characterizing the user’s connection to their ISP. Additionally, the last-mile is a significant portion of a broadband connection’s end to end latency. One of the active measurements we perform in C2E are traceroutes to remote destinations. Since all of these measurements traverse the user’s last-mile link, we aggregate across all measurements up until the first public IP hop. Note that if the ISP itself provides a NAT’d IP address, our measurements are going further into their network.
Next we’ll look at latency measurements performed from end systems in AT&T’s network. Here we only include users that have a wired connection in the last meter, to avoid the impact of wireless in the home network.

## Slide 7: Last-mile latency case study: AT&T
95% of AT&T users have a baseline latency < ~60ms
77% of AT&T users have a median latency < ~60 ms
Notes: This plot shows the distribution of last-mile latencies for C2E users in AT&T’s network. The solid blue and dotted green lines represent the per user minimum and median last-mile latency, respectively. Data from the SamKnows study showed that AT&T users had an average last-mile latency of 25 ms, represented by the vertical solid gray line. This sample had a standard deviation of 33 ms, the upper limit represented by the dotted gray line. We found that for approximately 95% of our users in AT&T’s network, their baseline latency fell within one standard deviation of the SamKnows findings, while 77% of our users had a median latency in this same range. Due to the similarity of these findings, we believe that C2E is able to accurately measure the last-mile latency.
Note: The average baseline(minimum) latency we found in our dataset was about 23 ms. This is within the 95% confidence interval of the SamKnows reported average.

## Slide 8: Measuring download throughput
Approach
  Use 30 second snapshots to passively monitor BitTorrent activity
    Ignore users with a download throughput cap
  Validate by comparing against the network diagnostic tool (NDT)
Dataset
  Discard users that were not actively downloading
  About 1,000 users in our dataset
Notes: Next we look at measuring download throughput. For each user, we collect a snap shot of BitTorrent activity every 30 seconds, which includes their current download speed. This also includes the user’s client configurations, such as whether or not they have a download or upload speed cap. When measuring download throughput, we ignore users with that throttle their download traffic. We also discard any users that were not actively downloading content.
Additionally, to provide a basis for comparison for our BitTorrent measurements, we also had users run the network diagnostic tool (NDT). With this subset of users, we are left with about 1,000 users in our dataset.

## Slide 9: Throughput – BT/NDT correlation
Strong correlation (r > 0.80) between NDT and BT max speeds
Notes: This plot shows a contour of the correlation between the maximum speeds measured from BitTorrent and NDT. In general, we find that as the users spend more time running BitTorrent (and run NDT a larger number of times), there is a higher correlation between download throughput measured by NDT and download throughput in BitTorrent.
For users with more than about 3 hours of BitTorrent activity (and 25 runs of NDT), we find a very strong correlation (greater than 0.8), between the two values.

## Slide 10: Throughput – BT/NDT Ratio
Cases where BT does not measure as high as NDT may be due to poorly seeded content
Notes: Here we look at the ratio between the throughput values measured by NDT and BitTorrent usage. The users to the left of 1 represent cases where NDT records a higher throughput rate, and the users to the right of 1 represent cases where BitTorrent achieves a higher throughput rate. For over 50% of the users, C2E measures higher throughput values using BitTorrent than NDT. In some of the extreme cases, the difference is due to the lack of a nearby measurement server.
We also see that for about 25% of users, BitTorrent measures a significantly lower speed than that reported by NDT. One potential cause of this is that the content a user is downloading is not very well seeded, or is only seeded by users with slower uplink capacity.
322 users

## Slide 11: Throughput – Including swarmspeed
BitTorrent speed >= 80% of fastest NDT value for 90% of users
Notes: One method that we’ve come up with to address this issue to calculate the total average swarm speed for all the torrents that a user is downloading. If a user is downloading a set of torrents where the average swarm speed is slower than their current download speed, we assume that the user is limited by the upload speeds of their connections. However, if the total average swarm speed is much higher, we assume that the user’s performance is limited by his or her broadband connection. As you can see, taking the swarm speed into consideration decreases the fraction of users that see a maximum BitTorrent throughput that is significantly slower than speeds measured by NDT.
Thus by adding the context of the application itself, we are able to get a better understand our passive measurements.
Note: It reduces number of users from about 300 to about 200 users when requiring a higher swarm speed

## Slide 12: Going back up
We just went “down” the stack to obtain these metrics, now can we go back “up” with another application?
Ran C2E in a controlled setting, simulating range of last-mile latencies and download capacities
  Actively last-mile latency and download a popular Linux ISO to measure download capacity
  Load 20 of the most popular websites in the US (ranked by alexa.com) to measure web performance
Notes: Now that I’ve explained how we go “down” the stack to obtain both download throughput and latency in BitTorrent, we want to go back “up” the stack and connect it with the user experience. For this purpose, we ran C2E in a controlled setting, simulating multiple download capacities and last-mile latencies. We used the previously described methods to measure both metrics, active traceroutes to measure last-mile latency and downloading content to measure throughput. To measure throughput, we downloaded a well seeded Linux ISO. Then, with the same network configuration, we repeatedly loaded alexa.com’s top 20 most popular websites in the US. In order to approximate the user’s experience in these tests, we measured the total page rendering time for each website.

## Slide 13: Web performance – Bandwidth
Small improvements in page rendering time after reaching 8 Mbps
Configured
Detected by C2E
Notes: In this plot we’ll look at page rendering time for four different websites. Here the y axis represents the page rendering time. The x represents the download throughput of the link. Note that the top value corresponds to the configured throughput rate and the bottom value is the throughput measured by C2E. Although the throughput values detected by C2E are generally lower, they are consistently within about 95% of the configured value.
We see that for a web page like craigslist, which had relatively few, small objects to retrieve, increasing download bandwidth did not benefit improve performance. Pages such as youtube, saw the largest gains from increasing bandwidth. However, for all 20 websites, improving download throughput beyond about 8 Mbps lead to to diminishing returns in improving performance.
Note that some pages saw an increase in page rendering time when increasing bandwidth. Since these tests were run over a fairly long period of time, changes in the content loaded on the front page, such as images or precached videos, may have affected the results. Additionally, each of the other 16 web pages showed a similar trend to one of these four sites.

## Slide 14: Web performance – Latency
Decreasing latency beyond ~30 ms does not have a significant impact
(Over 50% of users have a last-mile latency of less than 30 ms)
Notes: We repeated the same experiment for latency. Again, the y axis represents the page rendering time. This time, the x axis represnts the configured and C2E measured last-mile latency values, respectively. Here we see that decreasing the last-mile latency continues to improve performance, but only to a point. At about 30 ms, we see that decreasing last-mile latency any further leads to relatively small gains in page rendering time.

## Slide 15: Summary
By monitoring performance within an application and leveraging its context, we can obtain metrics that apply the performance of other applications
Next steps
  Extend work for other metrics (and how they affect each other)
    E.g. jitter, packet loss, DNS performance, service availability
  Deploy network application tests to users
    E.g. web browsing, video streaming
  Support C2E in other network-intensive applications
    E.g. Video streaming services, digital distribution platforms
Notes: So the main goal of this work was to show that we could take the performance of one application, and use it’s performance to relate it with another.
In the future, we plan to extend this to work to other metrics, such as jitter, packet loss, and DNS performance and measuring how different configurations of multiple settings affect page rendering time. We also plan to deploy our page web performance benchmark to C2E users, as well as tests for other applications such as video streaming.
We are also currently looking at implementing C2E in other network-intensive applications, such as video streaming and digital distribution platforms.
Thank you for attention; I’d be happy to answer any questions.